## Slide 1
MICRO CAUSES, MACRO EFFECTS
MICROSTRUCTURED SURFACES, INSTABILITIES, AND ASYMPTOTIC HOMOGENIZATION
Implications for thermal transport and management
Alessandro Bottaro
DICCA, Polytechnic School
University of Genova, Italy

## Slide 2: Why do microstructures matter?
Macroscopic transport is controlled by boundary conditions.
Boundary conditions are controlled by surface structure.
Surface structure is often microscopic.
Onset and amplification of instabilities are highly sensitive to boundary conditions.
Microscopic design can control macroscopic transport.

## Slide 3: Connection to thermal management
Thermal transport at surfaces is governed by near-wall transport processes.
Heat transfer depends on:
  boundary layer structure
  flow stability and transition
  transport coefficients
  surface geometry
Microstructured surfaces modify these mechanisms.
Understanding flow over structured surfaces enables control of heat transfer.

## Slide 4: Microstructures are ubiquitous in thermal systems
Examples include:
  Heat sinks with fins and grooves
  Microchannel cooling devices
  Structured hot/cold plates
  Porous and coated surfaces
Common feature: Transport is controlled by surface microgeometry.
GOAL: predict macroscopic flow without resolving microscopic details.

## Slide 5
THE THEORY

## Slide 6
Physical problem in a hierarchical system
Domain decomposition
Continuity of velocity and traction vectors
Asymptotic analysis of the microscale problem,
Closure problems are defined at different orders
Numerical solutions of the closure problems
Extrapolation to a matching interface at
Formal expressions of effective B.Cs
Solution evaluation at the matching interface

## Slide 7: A very quick primer
dimensionless microscopic coordinates
dimensionless macroscopic coordinates
dimensionless microscopic velocity scale
dimensionless macroscopic velocity scale
dimensionless (viscous) pressure in microdomain
dimensionless time
are assumed to be independent:
All dimensionless, microscopic dependent variables are written as

## Slide 8: The dimensionless Navier-Stokes equations in the microscale region are:
Note that at the macroscopic dimensionless velocity must be

## Slide 9: The dimensionless Navier-Stokes equations in the microscale region are:
At leading order in in the micro-domain we have:

## Slide 10: The boundary conditions of the microscopic problem at leading order are: plus periodicity in .
at the lower, rough wall in
at the upper boundary in
Separation of variables ansatz for the leading order variables:

## Slide 11: Plugging into the Stokes system, the closure problem for the variables at leading order becomes: subject to:
at
at

## Slide 12: Once the closure problem is solved and is known at we can retrieve the macroscopic slip velocity at
This boundary condition can then be Taylor-expanded to , at the outer rims of the roughness elements, to finally obtain, at leading order:
with the Navier slip tensor.

## Slide 13
For simple wall micro-structures such as those considered here:

## Slide 14: This procedure can be extended to higher orders …

## Slide 15
Advantages
computational cost
simplicity
optimization studies
advance in order
versatility

## Slide 17
Navier-slip condition
Second-order correction
Navier-slip condition
Second-order correction
Second-order,
effect of interface permeabilities
Second-order,
effect of medium permeability
Dimensionless effective boundary conditions at a porous interface
: Navier-slip coefficients

## Slide 20
PROBLEM 1:
BUOYANCY-INDUCED FLOW ALONG REGULARLY RIB-ROUGHENED VERTICAL SURFACES

## Slide 21
Problem 1:
Buoyancy-induced flow along regularly rib-roughened vertical surfaces

## Slide 22
Continuous ribs (examining different rib sizes/pitches).
Truncated ribs (examining different numbers of rib segments).
Agreement between experimental results and laminar simulations.
Validation of the homogenization-based effective boundary conditions.

## Slide 23
Transverse square ribs
Thermal slip coefficient and velocity-flux sensitivity parameter depend on rib-to-fluid thermal conductivity ratio
adiabatic ribs
perfectly conducting
ribs
wooden ribs

## Slide 25
Homogenized model (symbols)
vs.
Fully resolving sim. (dashed lines)
Average Nusselt number,
isothermal, smooth surface

## Slide 26
PROBLEM 2:
TURBULENCE OVER A MICROSTRUCTURED, POROUS WALL

## Slide 27
Problem 2:
Turbulence over a microstructured, porous wall

## Slide 29
-1
18
3.75
8.50
13.25

## Slide 31
smooth
Smooth
fully-resolving
model
model
fully-resolving

## Slide 32
Major parameters characterizing the mean velocity profile
mean streamwise velocity at the fluid-porous interface.
the roughness function.
upward shift drag reduction
downward shift drag increase

## Slide 33
Major parameters characterizing the mean velocity profile

## Slide 34
Drag increase
Possible drag reduction
for all

## Slide 35
PROBLEM 3:
FLOW THROUGH POROUS METAMATERIALS FORMED BY TPMS-BASED UNIT CELLS

## Slide 36: What are TPMS?
TPMS are mathematical surfaces that repeat periodically in three independent directions (like a 3D crystal lattice) while dividing space into two interpenetrating, labyrinthine regions.
They are "minimal" in the differential geometry sense: at every point, the mean curvature is exactly zero, meaning the surface is locally saddle-shaped and neither bulges inward nor outward.
The unifying reason nature converges on TPMS is elegant: they are the geometry that minimizes material use for a given surface area, while maintaining structural continuity in all three directions.
Examples in Nature: butterfly wing scales, cell membranes under stress, bone trabeculae, soap film systems, coral skeletons …

## Slide 37
TPMS-based unit cells

## Slide 38: Some applications
The key insight is that both fluids are simultaneously continuous throughout the volume — neither is trapped in discrete tubes — giving a vastly larger contact area than any shell-and-tube design of the same envelope size.
Compact heat exchangers (e.g. recuperators, electronics cooling): their continuous geometry allows two fluids to flow through interpenetrating channels simultaneously with enormous interfacial area.
Phase-change systems (evaporators, condensers): the smooth, continuously curved surface promotes uniform thin-film flow and delays dry-out, while the high tortuosity enhances mixing without excessive pressure drop.
Heat sinks for high-flux electronics and battery thermal management: tunable porosity and isotropic thermal conductivity allow precise balancing of heat dissipation and coolant pumping power across complex geometries.
Hydrofoils and turbine blades: a gyroid-structured extension attached to a hydrofoil trailing edge can prevent the formation of Kármán vortices and remarkably reduce vortex-induced vibration.

## Slide 39
Problem 3:
Flow through porous metamaterials formed by TPMS-based unit cells
Metamaterials
Artificially engineered media, designed and fabricated to attain unique properties allowing them to offer novel functionalities, often unachievable by conventional materials.
- are self-standing, highly interconnected, lightweight, and manufacturable by 3D printing
- may have unique topological, acoustic, hydrodynamic, and mechanical features.
TPMS-based structures
Darcy’s law
Classical version
Upgraded version
Stokes’ conditions
Intrinsic permeab.
(𝒦)
Inertial effects
Effective permeab.
(𝓗)
Sensitive to
geometry
Sensitive to
geometry & Re

## Slide 40
Microscopic length scale
Macroscopic length scale
Fast spatial variables
Slow spatial variables
Macroscopic pressure gradient
Magnitude
Unit vector
,
Closure problem
closure variable

## Slide 41
Effect of the medium porosity on
in air for
Forchheimer regime

## Slide 42
PROBLEM 4:
TAYLOR-COUETTE INSTABILITIES WITH RIBBED SURFACES

## Slide 43: Problem 4: Taylor-Couette instability with ribbed surfaces
d = gap between the cylinders
Ri/o = inner/outer radius
Shaft
Outer cylinder
Inner cylinder:
steel cylinder + grooved skeleton
Air bearing
2 shapes (Square and Trapezoidal)
3 periodicity ( = 1000, 800, 400 μm)

## Slide 44: TAYLOR-COUETTE FLOW AND INSTABILITIES
When the slope changes,
secondary flows appear modifying
the shear stress. The corresponding
speed is called “critical”.
Determine whether specific surface patterns can delay or
anticipate the onset of the primary Taylor-Couette instability.
AIM

## Slide 45: THEORETICAL APPROACH
Asymptotic homogenization theory for effective boundary conditions
Microscopic length
Macroscopic length
Axially periodic and azimuthally invariant microgrooves
Use of
homogenization theory
Definition of
effective boundary conditions
at a virtual wall

## Slide 46
In order to evaluate azimuthal slip length
and spanwise slip length‘realistic’ shapes
have been defined.
The azimuthal slip length defines
the virtual origin of the mean flow.

## Slide 47
…using virtual coordinates, the curves collapse in the low-Ta range!
EXPERIMENTAL RESULTS
Defect on S800
Trapezoidal
Square

## Slide 48
Variations of critical parameters with respect to the no-slip case versus Δ/dvrt
Idealized shape
Realistic shape
Square
Trapezoidal
Stability results
The largest increase in critical parameters is achievable
by the use of microgrooves maximizing ∆.
LINEAR STABILITY RESULTS IN VIRTUAL COORDINATES

## Slide 49
TAKE HOME MESSAGE

## Slide 50
TAKE HOME MESSAGE
Understanding the effects of microstructures enable:
Predictive design
Efficient modeling
Passive transport control
Asymptotic methods provide powerful engineering tools to model and optimize microscopic structures without heavy numerical requirements.
Microscopic structure modifies effective physics.
Effective physics determines macroscopic transport.
Micro causes, macro effects