## Slide 1: Tip clearance CFD models to improve the aerodynamic characterization of heavy duty gas turbine transonic axial compressors
Candidate: Luca Ottonello
Supervisor Prof. Ing. Alessandro Bottaro
Co-Supervisor: Ing. Savino Depalo

## Slide 2: Index
Objective
Importance of compressor stability
Method of investigation:
  Flow chart
Methodology
Compressor 1 results
  Numerical convergence & mass flow analysis
  Speedlines
  Speedlines for most critical stages
  Streamlines for row “C”
Compressor 2 results
  Numerical convergence & mass flow analysis
  Speedlines
  Speedlines for most critical stages
  Streamlines for row “B”
Results summary
Conclusions

## Slide 3: Objective
Main goal: better understanding of tip clearance flow, updating CFD calculation setup on turbo-axial compressors for more reliable surge margin detection.
New clearance model to improve the mass flow conservation between SS and PS of every blade:
NEW OPENTIP
H-PINCH
SBLOCK

## Slide 4: Importance of compressor stability
TG Efficiency;
Operating range (Over/under-frequencies, ambient temperature variation and partial load);
Surge Margin & Surge line.
IGV Fixed

## Slide 5: Importance of compressor stability
Two different phenomena contribute to reduce the compressor operating range:
Spike stall
Short length scale disturbance marked by the formation of three dimensional, finite amplitude disturbances, localized to the tip region of just one rotor of a multistage compressor.
Modal stall
Long length scale disturbance that extend axially through the compressor, which evolves until it becomes a fully developed stall cell.

## Slide 6: Method of Investigation
Flow chart
Baldwin – Lomax turbulence model
NRBC mixing plane
Ideal gas
H-Mesh type
CFD
Clearance model analysis
Old Opentip
New Opentip
Sblock
H-Pinch
Setup F
Compressor 1
Test case
Compressor 2
Test case
Results
&
discussion

## Slide 7: Methodology
All the models take advantage of “morphed” mesh: local warp to better discretize the clearance region profile:
Old Opentip
The clearance region is not computed;
Periodicity model through the imposition of a periodic boundary condition.
T.E.
L.E.

## Slide 8: Methodology
New Opentip
New simplified model developed applying a correction on the BC ;
Correction applied to the velocity magnitude value in the phantom cells;
Performed through the “clear.bat” file.
Enforcing BC as in the previous model
Evaluating mass Flow Unbalance (∆)
Modifying Velocity Magnitude on phantom Cells to enforce ∆
Updating ρEt and p using the modified velocity field

## Slide 9: Methodology
Sblock
The only model which allows to mesh clearance;
Fully solving of clearance flow field and preserve the mass flow between inlet and outlet of every row;
Performed running “Sblock code”.
H-Pinch
Blade tip pinched geometry mismatch w.r.t. actual one;
Avoid the application of conservation law through geometrical expedient to make a correspondence between SS and PS;
Performed running the “Pinch code”.

## Slide 10: Compressor 1 results
Numerical convergence & mass flow analysis
Improvement in term of average error for all models;
Improvement in mass flow conservation for all new clearance models.
 | Old Opentip | New Opentip | H-Pinch | Sblock
Eq Time w.r.t. Old model (%) | 100 | 72.6 | 25.5 | 26.5
Avg error [-]
0 500 1000 1500 2000 2500 3000
-5.2
-5.4
-5.6
-5.8
-6
-6.2
-6.4
-6.6
-6.8
Iteration [-]
-1.8
0
-0.2
-0.4
-0.6
-0.8
-1
-1.2
-1.4
-1.6
0.2
Mass flow error [Kg/s]
20 25 30 35 40 45
#Row
Old Opentip
New Opentip
H-Pinch
Sblock

## Slide 11: Compressor 1 results
Speedlines
All the models show a choked characteristic;
Old Opentip and New Opentip models are aligned, other models underline an higher SM;
Old Opentip is the model showing the smallest surge margin.
0.9992 0.9994 0.9996 0.9998 1 1.0002 1.0004 1.0006 1.0008 1.001
1.025
1.02
1.015
1.01
1.005
1
MF [-]
∆SM [-]
Old Opentip
H-Pinch
New Opentip
Sblock
WP
SP

## Slide 12: Compressor 1 results
M* [-]
M* [-]
M* [-]
∆SM [-]
∆SM [-]
Speedlines for most critical stages
Sblock
Pinch
New Opentip
Critical stages detected where the ∆SM–M* characteristic become flattering :
B stage;
C stage;
D stage.
∆SM [-]
STG-A
STG-B
STG-C
STG-D
WP
SP

## Slide 13: Compressor 1 results
Streamlines for row “C”:
Sblock
H-Pinch
New Opentip
Old Opentip
FLOW

## Slide 14: Compressor 2 results
Numerical convergence & mass flow analysis
Improvement in mass flow conservation for all new models tested;
Increasing in average error for Sblock and New Opentip model w.r.t. the Old Opentip one.
 | Old Opentip | New Opentip | Sblock
Eq Time w.r.t. Old model (%) | 100.0 | 72.7 | 68.0
Mass flow error [Kg/s]
0.2
0.1
0
-0.3
-0.4
-0.5
-0.2
-0.1
#Row
10 5 10 15 20 25 30
Avg error [-]
-2
-3
-4
-5
-6
-7
-8
0 1000 2000 3000 4000 5000
Iteration [-]
Old Opentip
New Opentip
Sblock

## Slide 15: Compressor 2 results
Speedlines
Sblock is the model showing the smallest surge margin, with the aim to offer a better visualization, were performed two point to the choke;
New Opentip is the model closest to Old Opentip from the surge margin point of view.
Old Opentip
New Opentip
Sblock
WP
SP
∆SM [-]
0.988 0.99 0.992 0.994 0.996 0.998 1 1.002 1.004
1.12
1.1
1.08
1.06
1.04
1.02
1
0.98
0.96
MF [-]

## Slide 16: Compressor 2 results
∆SM [-]
∆SM [-]
∆SM [-]
Speedlines for most critical stages
Old Opentip
New Opentip
Sblock
Critical stages detected where the ∆SM–M* characteristic become flattering :
B
∆SM-M*
STG-E
STG-B
STG-C
STG-D
STG-A
WP
SP
M* [-]
M* [-]
M* [-]

## Slide 17: Compressor 2 results
Streamlines for row “B”:
FLOW
Old Opentip
New Opentip
Sblock

## Slide 18: Results Summary
 | New Opentip | Sblock | H-Pinch
∆MF Inlet (kg/s) | -0.10 | -0.10 | -1.20
∆T out (K) | 0.80 | 2.50 | 4.20
∆SM (%) | 0.30 | 2.90 | 1.90
∆η_pol – overall (%) | -0.07 | -0.23 | -0.35
Compressor 1
 | New Opentip | Sblock
∆MF Inlet (kg/s) | -0.60 | 2.69
∆T out (K) | 0.53 | 1.09
∆SM (%) | -6.30 | -12.3
∆η_pol – overall (%) | -0.06 | -0.17
Compressor 2
Chart: ∆T out (K)
| Compressor 1 | Compressor 2
New Opentip | 0.8 | 0.53
Sblock | 2.5 | 1.09
H-Pinch | 4.2
Chart: ∆SM (%)
| Compressor 1 | Compressor 2
New Opentip | 0.3 | -6.3
Sblock | 2.9 | 2.69
H-Pinch | 1.9

## Slide 19: Conclusions
Sblock: best progress in term of clearance analysis, and when it is possible, can be applied, providing the best and more accurate results;
New Opentip: the simplest model, natural evolution of the Old model, a good numerical convergence together with a better mass flow conservation can be achieved, it can be applied as an alternative to Sblock model, because of its peculiar robustness;
H-Pinch: represents the most problematic model as a consequence of the different secondary fluxes modelling caused by the particularly way of treating the clearance region, it is not recommended to apply it, with the exclusion of special cases.
TG stability
Compressor operative range influenced by secondary fluxes
More reliable results through new clearance models

## Slide 20
Thank you for your attention

## Slide 21: The importance of clearance flow
Spike stall is the problem that determines, more than anything else, the malfunctioning of the compressor and it is localized at the clearance, phenomenon strongly related to two flow events:
1) Leading-edge tip-clearance flow spillage below the blade tip
2) Back flow of tip-clearance fluid below the blade tip

## Slide 22: Results Summary
 | New Opentip | Sblock | H-Pinch
∆MF Inlet (kg/s) | -0.10 | -0.10 | -1.20
∆T out (K) | 0.80 | 2.50 | 4.20
∆SM (%) | 0.30 | 2.90 | 1.90
∆η_pol – overall (%) | -0.07 | -0.23 | -0.35
Compressor 1
 | New Opentip | Sblock
∆MF Inlet (kg/s) | -0.60 | 2.69
∆T out (K) | 0.53 | 1.09
∆SM (%) | -6.30 | -12.3
∆η_pol – overall (%) | -0.06 | -0.17
Compressor 2
Chart: ∆T out (K)
| Compressor 1 | Compressor 2
New Opentip | 0.8 | 0.53
Sblock | 2.5 | 1.09
H-Pinch | 4.2
Chart: ∆SM (%)
| Compressor 1 | Compressor 2
New Opentip | 0.3 | -6.3
Sblock | 2.9 | 2.69
H-Pinch | 1.9
Chart: ∆MF Inlet (kg/s)
| Compressor 1 | Compressor 2
New Opentip | -0.1 | -0.6
Sblock | -0.1 | 2.69
H-Pinch | -1.2
Chart: ∆η_pol-overall (%)
| Compressor 1 | Compressor 2
New Opentip | -0.07 | -0.06
Sblock | -0.23 | -0.17
H-Pinch | -0.35